## Slide 1: Visualizing Northshore Watershed Topology and Flow Patterns
James E. Mitchell, Ph.D.
IT GIS Manager
Adapted from a Presentation at the
2012 ESRI International User’s Conference
San Diego, California – July, 2012 (Revised January, 2013)
Notes: Presentation by James E. Mitchell, Ph. D. at the 2012 State of The Coast Conference, sponsored by the Coalition for Coastal Louisiana, New Orleans, LA, June 25, 2012.

## Slide 2: The Watershed Boundary Database
A national database defining hydrologic boundaries
  Based on the USGS Hydrologic Unit Codes
Hierarchical organization that aggregates basins into
  Regions – “HUC 2”
  Subregions – “HUC 4”
  Basins – “HUC 6”
  Subbasins – “HUC 8”
  Watersheds – “HUC 10”
  Subwatersheds – “HUC 12”
An areal depiction of the organization of watersheds and the flow of water across the landscape

## Slide 3
Lake Pontchartrain Basin from the WBD Database
“Out of the box,” it is easy to see basin delineations. However, flow direction is less evident. As complexity increases and topography decreases relationships are unclear.

## Slide 4
Lake Pontchartrain Basin Symbolized by HUC 10 Basins
Drainage patterns are more evident, using symbology. However detail is still lacking and relationships in complex areas are not clearly revealed.

## Slide 5
Lake Pontchartrain Basin Showing WBD Downstream Topology
A schematic visualization of the Lake Pontchartrain Basin drainage pattern. This clearly depicts the drainage network in geographic space.

## Slide 6: What Can Be Done with this Schematic Diagram?
Explore WBD Relationships
Identify flow relationships
  Upstream/downstream (including multiple pourpoints
  Flow accumulation
  Diversions and interbasin transfers
Visualize the flow network in different formats (styles)
Trace flow paths
  Connect sources to downstream impacts

## Slide 7
Flow Topology Applications
Connecting Upstream and Downstream
Schematic diagrams can be “traced” and selections propagated into the data frame

## Slide 8
Lake Pontchartrain Basin Geographic and Schematic Diagrams
Maps and diagrams are linked allowing selections to be propagated between them. The schematic depiction of these basins provides a clear view of their topology

## Slide 9
Lake Pontchartrain Basin Hierarchical Smart Tree Diagram
The diagram provides a simplified depiction of the topology of the Lake Pontchartrain Basin. Up and downstream traces can be executed and transferred to the map.

## Slide 10
Lake Pontchartrain Basin Hierarchical Diagram/Orthogonal Corners
Diagrams can be edited and reformatted using varies options. Using this capability, diagrams can be designed to satisfy essential operational and functional requirements.

## Slide 11: Conclusions
Schematics provide a powerful tool for visualizing topological relationships
  “Geographic” (map) space
  “Logical” (diagram) space
Schematics can be used to investigate, reconcile, and explore topological relationships
Schematics can be used to extend the capabilities of geospatial data, such as the Watershed Boundary Dataset by:
  Creating a logical network representing the flow through geographic elements
  Augmenting simple topology with complex networks
  Extending the capabilities of the data with tools that can navigate through the network

## Slide 12: For More Information
Contact
James E. Mitchell, Ph. D.
Louisiana Office of Technology Services
jim.mitchello@la.gov 225-379-1881